## Slide 1: Title: Fundamentals of Computer Design Subtitle: Chapter 1 Overview Course Name: BCT 2408 Computer Architecture Your Name: Enoch Teddy ADM NO: SCT212-0078/2021

## Slide 2: Introduction to Computer Architecture
What is Computer Architecture?
Computer architecture refers to the structure and organization of the components in a computer system.
It includes both the hardware and software components that enable the execution of programs.
Key Focus Areas:
Performance: Achieving desired levels of speed and efficiency.
Cost: Designing systems that are affordable.
Power: Minimizing power consumption, especially for mobile devices.
Design Goals:
Design computers to perform tasks with high performance while maintaining energy efficiency and cost-effectiveness.

## Slide 3: Evolution of Computer Design
Early Computers:
  Early computers like the ENIAC used vacuum tubes and were slow, large, and inefficient.
  The shift to transistors (in the 1950s) revolutionized computing, offering faster speeds and more compact designs.
Integrated Circuits:
  The invention of integrated circuits (ICs) in the 1960s further reduced the size and cost of computers and allowed for increased reliability.
Microprocessors:
  In the 1970s, the development of microprocessors led to the creation of personal computers, making computing accessible to individuals and small businesses.
Modern Advancements:
  Today, multi-core processors, parallelism, and energy efficiency are the major trends in computer design.

## Slide 4: Classes of Computers
General-Purpose Computers:
  Can perform a wide variety of tasks. Examples: Desktops, laptops, workstations.
  Versatile and user-friendly but may not be optimized for specific tasks.
Embedded Systems:
  Designed for specific, often real-time, applications. Examples: Microwave ovens, cars, digital cameras, smart thermostats.
  These systems are energy-efficient and cost-effective but typically not very flexible in terms of functionality.
Supercomputers:
  The most powerful systems in terms of processing power. Used for highly complex computations such as climate modeling, simulations, or molecular research.
  Can perform billions of calculations per second.
Servers:
  Provide resources or services to other computers (clients) on a network. Examples: Web servers, file servers, database servers.
  Designed to handle high workloads, manage large amounts of data, and support multiple users simultaneously.
Client-Server Model:
  Clients: Request services from the server (e.g., web browsers, email clients).
  Servers: Provide data or services to clients (e.g., web servers, mail servers).

## Slide 5: Defining Computer Architecture
Computer Architecture (Definition):
Computer architecture refers to the design of a computer system’s instruction set, the interaction between the components, and how those components are connected.
Key Components:
Instruction Set Architecture (ISA): The ISA is the interface between hardware and software. It defines the set of operations the CPU can perform and the way software can interact with the hardware. Examples of ISAs: x86, ARM, MIPS.
Performance Metrics:
  Clock Speed: The rate at which a processor executes instructions, measured in GHz (Gigahertz).
  Throughput: The amount of work completed over time (e.g., instructions per second).
  Latency: The time it takes to complete a single task (e.g., time from issuing a command to receiving a result).
Memory Hierarchy:
  multi-level structure of memory components ranging from fast and expensive (registers, caches) to slow and cheap (hard drives, network storage). Optimizing memory hierarchy is crucial for improving performance.
I/O Systems:
  Input and Output (I/O) systems are responsible for communication between the computer and external devices.
  Common I/O devices include keyboards, displays, network interfaces, and storage devices.
Design Trade-offs:
Designing a computer architecture involves making trade-offs between performance, cost, and power consumption. For example, more cores in a processor can increase performance but consume more power and increase cost.

## Slide 6: Trends in Technology
Miniaturization:
As technology advances, the size of computer components continues to shrink, resulting in smaller, more powerful devices. Example: From vacuum tubes to transistors to integrated circuits.
Moore's Law:
The number of transistors on a microchip doubles approximately every two years, which increases processing power and enables more complex systems at lower costs.
Energy Efficiency:
As transistor density increases, managing power consumption becomes crucial to avoid overheating and to improve battery life in mobile devices.
Parallelism: As clock speeds hit physical limits, processors increasingly rely on parallelism to achieve performance improvements.
Multi-core processors allow for multiple tasks to be executed simultaneously, improving throughput and reducing latency for multi-threaded workloads.
Vector processors and GPUs are specialized for certain kinds of parallel computation (e.g., graphics rendering or scientific computing).

## Slide 7: Performance, Power, and Cost Trade-offs
Performance:
Achieving high performance is a primary goal in computer architecture. Performance can be measured by throughput (tasks per second) or latency (time per task).
Performance vs. Power: Higher performance can lead to increased power consumption. For example, more cores and higher clock speeds result in greater power usage.
Cost Considerations:
More complex systems cost more to manufacture, both in terms of hardware and power consumption.
Engineers must balance performance and power demands with available budget constraints.
The Role of Technology Scaling:
As technology improves, new materials and designs lead to more efficient and powerful systems at lower costs.

## Slide 8: Key Metrics for Computer Performance
Clock Speed:
The speed at which a processor executes instructions, measured in hertz (Hz). Higher clock speeds generally lead to faster execution, but they also increase power consumption.
Throughput:
The amount of work a system can complete in a given time period. A key performance metric, particularly for systems with multiple processors.
Latency:
The time taken for a single task to complete, which impacts system responsiveness.
Amdahl’s Law:
Formula: Speedup=1/((1−P)+(P/N)) Describes the maximum improvement in performance that can be achieved when only part of a system is improved (e.g., adding more processors).

## Slide 9: Impact of Technology on Computer Design
Shift from Single-Core to Multi-Core Systems:
Multi-core processors enable parallelism, improving performance without significantly increasing clock speeds.
Energy-Efficient Design:
Modern computing emphasizes low power designs to minimize energy usage, reduce heat, and extend battery life in mobile devices.
Customization for Specialized Tasks:
Increasingly, processors are optimized for specific applications:
  GPUs for graphics and machine learning.
  ASICs for tasks like cryptocurrency mining or network routing.
Cloud Computing and Virtualization:
Cloud services require the design of scalable, efficient systems capable of handling massive amounts of data and user requests.